## Slide 1: Cache Memory
Lecture 03
Instructor: Tapushe Rabaya Toma
SWE, DIU.

## Slide 2: Reference Books
Computer Organization and Architecture: Designing for Performance- William Stallings (8th Edition)
  Any later edition is fine

## Slide 3: Performance of Memory
Based on three performance parameters
Access time (latency): For random-access memory, this is the time it takes to perform a read or write operation
  For non-random-access memory, access time is the time it takes to position the read–write mechanism at the desired location
Memory cycle time: This concept is primarily applied to random-access memory and consists of the access time plus any additional time required before a second access can commence
  This additional time may be required for transients to die out on signal lines or to regenerate data if they are read destructively
Transfer rate: This is the rate at which data can be transferred into or out of a memory unit
  For random-access memory, it is equal to 1/(cycle time)

## Slide 4: Performance of Memory
For non-random-access memory, the following relationship holds:
where
  TN = Average time to read or write N bits
  TA = Average access time
  n = Number of bits
  R = Transfer rate, in bits per second (bps)
Several physical characteristics of memory are also important

## Slide 5: The Memory Hierarchy
Depends on:
Faster access time, greater cost per bit
Greater capacity, smaller cost per bit
Greater capacity, slower access time

## Slide 6: Cache Memory Principles

## Slide 7: Cache Memory Principles
The cache contains a copy of portions of main memory
When the processor attempts to read a word of memory, a check is made to determine if the word is in the cache. If so, the word is delivered to the processor
If not, a block of main memory, consisting of some fixed number of words, is read into the cache and then the word is delivered to the processor
When a block of data is fetched into the cache to satisfy a single memory reference, it is likely that there will be future references to that same memory location or to other words in the block
  Locality of reference

## Slide 8: Cache Memory Structure

## Slide 9: Cache Read Operation

## Slide 10: Typical Cache Organization

## Slide 11: Elements Of Cache Design

## Slide 12: Cache Addresses

## Slide 13: Mapping Technique
Performance of the cache memory mapping function
is key to the speed
• There are a number of mapping techniques
– Direct mapping
– Associative mapping
– Set associative - mapping

## Slide 14: Direct Mapping
The mapping is expressed as:
where
  i= cache line number
  j = main memory block number
  m = number of lines in the cache

## Slide 15: Mapping Mechanisms

## Slide 16: Mapping Mechanisms

## Slide 17: Direct Mapping Technique

## Slide 18: Direct Mapping Example

## Slide 19: Direct Mapping Example
Advantage and Disadvantage?
  Refer to text book

## Slide 20: Fully Associative Cache Example

## Slide 21: Fully Associative Cache Example
Advantage and Disadvantages?
  Refer to textbook

## Slide 22: Set-associative Mapping

## Slide 23: Set-associative Mapping (2- way set.)

## Slide 24: Replacement Algorithms
Once the cache has been filled, when a new block is brought into the cache, one of the existing blocks must be replaced
For direct mapping, there is only one possible line for any particular block, and no choice is possible
For the associative and set-associative techniques, a replacement algorithm is needed
  To achieve high speed, such an algorithm must be implemented in hardware

## Slide 25: Replacement Algorithms
Least Recently Used (LRU)
  Most effective
First-in-First-Out (FIFO)
Least Frequently Used (LFU)
For details: Find the book and study!

## Slide 26: Write Policy
When a block that is resident in the cache is to be replaced, there are two cases to consider
If the old block in the cache has not been altered, then it may be overwritten with a new block without first writing out the old block
If at least one write operation has been performed on a word in that line of the cache, then main memory must be updated by writing the line of cache out to the block of memory before bringing in the new block

## Slide 27: Write Policy
Two potential problems
More than one device may have access to main memory
If multiple processors are attached to the same bus and each processor has its own local cache

## Slide 28: Write Policies
Write through
  Simplest of all
Write back
  Minimizes memory writes (dirty bit or use bit)

## Slide 29: Write Policies
In a bus organization in which more than one device (typically a processor) has a cache and main memory is shared, a new problem is introduced
If data in one cache are altered, this invalidates not only the corresponding word in main memory, but also that same word in other caches
A system that prevents this problem is said to maintain cache coherency

## Slide 30: Write Policies
Solutions:
  Bus watching with write through
  Hardware transparency
  Non-cacheable memory

## Slide 31: Thanks!