## Slide 1: Advanced Processor Architecture
Lecture 05
Instruction Set
Processor Structure
Instructor: Tapushe Rabaya Toma
Lecturer, SWE, DIU

## Slide 2: Reference Books
Computer Organization and Architecture: Designing for Performance- William Stallings (8th Edition)
  Any later edition is fine

## Slide 3: Addressing Techniques
Depends on trade-off between address range and/or addressing flexibility, and the number of memory references in the instruction and/or the complexity of address calculation
  Immediate
  Direct
  Indirect
  Register
  Register indirect
  Displacement
  Stack

## Slide 4: Addressing Techniques

## Slide 5: Addressing Techniques

## Slide 6: Addressing Techniques

## Slide 7: Addressing Techniques
Virtually all computer architectures provide more than one of these addressing modes
  Often, different opcodes will use different addressing modes
  Also, one or more bits in the instruction format can be used as a mode field
Effective address (EA): In a system without virtual memory, the effective address will be either a main memory address or a register
In a virtual memory system, the effective address is a virtual address or a register
The actual mapping to a physical address is a function of the memory management unit (MMU) and is invisible to the programmer

## Slide 8: Internal Structure of the CPU

## Slide 9: Register Organization
The registers in the processor perform two roles:
  User-visible registers: Enable the machine-or assembly language programmer to minimize main memory references by optimizing use of registers
  Control and status registers: Used by the control unit to control the operation of the processor and by privileged, operating system programs to control the execution of programs

## Slide 10: User-Visible Registers
Could be categorized into following categories:
  General purpose
  Data
  Address
  Condition codes
GP registers can be assigned to a variety of functions by the programmer
  Any general-purpose register can contain the operand for any opcode
  Can be used for addressing functions (e.g., register indirect, displacement)

## Slide 11: User-Visible Registers
Data registers may be used only to hold data and cannot be employed in the calculation of an operand address
Address registers may themselves be somewhat general purpose, or they may be devoted to a particular addressing mode
Such as:
  Segment pointers: Holds the address of the base of the segment.
  Index registers: These are used for indexed addressing and may be auto indexed
  Stack pointer: If there is user-visible stack addressing, then typically there is a dedicated register that points to the top of the stack
  This allows implicit addressing; that is, push, pop, and other stack instructions need not contain an explicit stack operand

## Slide 12: User-Visible Registers
A partially visible registers, which hold condition codes (also referred to as flags)
Condition codes are bits set by the processor hardware as the result of operations
Example: An arithmetic operation may produce a positive, negative, zero, or overflow result
In addition to the result itself being stored in a register or memory, a condition code is also set
The code may subsequently be tested as part of a conditional branch operation

## Slide 13: Control and Status Registers
Four main categories:
Program counter (PC): Contains the address of an instruction to be fetched
Instruction register (IR): Contains the instruction most recently fetched
Memory address register (MAR): Contains the address of a location in memory
Memory buffer register (MBR): Contains a word of data to be written to memory or the word most recently read

## Slide 14: Control and Status Registers
Program Status Word (PSW)
Contains condition codes plus other status information. Common fields or flags include the following:
  Sign: Contains the sign bit of the result of the last arithmetic operation
  Zero: Set when the result is 0
  Carry: Set if an operation resulted in a carry (addition) into or borrow (subtraction) out of a high-order bit
  Equal: Set if a logical compare result is equality
  Overflow: Used to indicate arithmetic overflow
  Interrupt Enable/Disable: Used to enable or disable interrupts
  Supervisor: Indicates whether the processor is executing in supervisor or user mode

## Slide 15: Data Flow
Figure: Data Flow, Fetch Cycle

## Slide 16: Data Flow
Figure: Data Flow, Indirect Cycle

## Slide 17: Data Flow
Figure: Data Flow, Interrupt Cycle

## Slide 18: Instruction Pipelining
Similar to the use of an assembly line in a manufacturing plant
An instruction has a number of stages
Figure: Two-Stage Instruction Pipeline

## Slide 19: Instruction Pipelining
This pipeline has two independent stages
  The first stage fetches an instruction and buffers it
  When the second stage is free, the first stage passes it the buffered instruction
While the second stage is executing the instruction, the first stage takes advantage of any unused memory cycles to fetch and buffer the next instruction
This is called instruction prefetch or fetch overlap

## Slide 20: Instruction Pipelining
Speed-up is unlikely for two reasons:
The execution time will generally be longer than the fetch time
  Fetch stage may have to wait for some time before it can empty its buffer
A conditional branch instruction makes the address of the next instruction to be fetched unknown
  Fetch stage must wait until it receives the next instruction address from the execute stage
The execute stage may then have to wait while the next instruction is fetched

## Slide 21: Instruction Pipelining
Solution for problem 2:
Guessing can reduce the time loss.
When a conditional branch instruction is passed on from the fetch to the execute stage, the fetch stage fetches the next instruction in memory after the branch instruction
  Then, if the branch is not taken, no time is lost
  If the branch is taken, the fetched instruction must be discarded and a new instruction fetched

## Slide 22: Instruction Pipelining
Stages of instruction processing
  Fetch instruction (FI): Read the next expected instruction into a buffer
  Decode instruction (DI): Determine the opcode and the operand specifiers
  Calculate operands (CO): Calculate the effective address of each source operand. This may involve displacement, register indirect, indirect, or other forms of address calculation
  Fetch operands (FO): Fetch each operand from memory. Operands in registers need not be fetched
  Execute instruction (EI): Perform the indicated operation and store the result,if any, in the specified destination operand location
  Write operand (WO): Store the result in memory

## Slide 23: Instruction Pipelining

## Slide 24: Instruction Pipelining
Several other factors limit the performance
  If the six stages are not of equal duration, there will be some waiting involved at various pipeline stages
  Another difficulty is the conditional branch instruction, which can invalidate several instruction fetches

## Slide 25: Instruction Pipelining

## Slide 26: Instruction Pipelining
Flowchart:
Six-Stage CPU Instruction Pipeline

## Slide 27: Instruction Pipelining
Though it might appear that the greater the number of stages in the pipeline, the faster the execution rate
At each stage of the pipeline, there is some overhead involved in moving data from buffer to buffer and in performing various preparation and delivery functions
  This overhead can appreciably lengthen the total execution time of a single instruction
This is significant when sequential instructions are logically dependent, either through heavy use of branching or through memory access dependencies
The amount of control logic required to handle memory and register dependencies and to optimize the use of the pipeline increases enormously with the number of stages
Another consideration is latching delay: It takes time for pipeline buffers to operate and this adds to instruction cycle time

## Slide 28: Pipeline Hazards
A pipeline hazard occurs when the pipeline, or some portion of the pipeline, must stall because conditions do not permit continued execution
Referred to as also a pipeline bubble
There are three types of hazards:
  Resource
  Data and
  Control

## Slide 29: Pipeline Hazards
Resource Hazards: A resource hazard occurs when two (or more) instructions that are already in the pipeline need the same resource
The result is that the instructions must be executed in serial rather than parallel for a portion of the pipeline
Sometime referred to as a structural hazard

## Slide 30: Pipeline Hazards
What happens when multiple instructions are ready to enter the execute instruction phase and there is a single ALU?
Read the book!

## Slide 31: Pipeline Hazards
Data Hazards: Occurs when there is a conflict in the access of an operand location
Two instructions in a program are to be executed in sequence and both access a particular memory or register operand
If the two instructions are executed in strict sequence, no problem occurs
However, if the instructions are executed in a pipeline, then it is possible for the operand value to be updated in such a way as to produce a different result than would occur with strict sequential execution
In other words, the program produces an incorrect result because of the use of pipelining

## Slide 32: Pipeline Hazards
Three types of data hazards
Read after write (RAW), or true dependency: An instruction modifies a register or memory location and a succeeding instruction reads the data in that memory or register location
  A hazard occurs if the read takes place before the write operation is complete
Write after read (WAR), or anti-dependency: An instruction reads a register or memory location and a succeeding instruction writes to the location
  A hazard occurs if the write operation completes before the read operation takes place
Write after write (WAW), or output dependency: Two instructions both write to the same location
  A hazard occurs if the write operations take place in the reverse order of the intended sequence

## Slide 33: RAW Data Hazard

## Slide 34: Pipeline Hazards
Control Hazards: Also known as a branch hazard, occurs when the pipeline makes the wrong decision on a branch prediction and therefore brings instructions into the pipeline that must subsequently be discarded

## Slide 35: Thank you!