## Slide 1: Computer Architecture
Lecture 04
Computer Arithmetic &
Instruction Set
Instructor: Tapushe Rabaya Toma
Sr. Lecturer, SWE, DIU

## Slide 2: Reference Books
Computer Organization and Architecture: Designing for Performance- William Stallings (8th Edition)
  Any later edition is fine

## Slide 3: ALU
Data are presented to the ALU in registers, and the results of an operation are stored in registers
The ALU may also set flags as the result of an operation
The flag values are also stored in registers within the processor
The control unit provides signals that control the operation of the ALU and the movement of the data into and out of the ALU

## Slide 4: Number Representation (Fixed Point)
Integer Representation
  Straight forward, can not present signed numbers
Sign-Magnitude Representation
  If the sign bit is 0, the number is positive; if the sign bit is 1, the number is negative
Disadvantages:
  Addition and subtraction require a consideration of both the signs of the numbers and their relative magnitudes to carry out the required operation
  There are two representations of 0

## Slide 5: Number Representation (Fixed Point)
Twos Complement Representation
  Mostly used

## Slide 6: Converting between Different Bit Lengths
This is called sign extension

## Slide 7: Block Diagram of Hardware for Addition and Subtraction

## Slide 8: Multiplication Implementation

## Slide 9: Multiplication Implementation

## Slide 10: Multiplication (Unsigned) Implementation

## Slide 11: Multiplication (2’s Complement) Implementation

## Slide 12: Multiplication (2’s Complement) Implementation

## Slide 13: Flowchart for Unsigned Binary Division

## Slide 15: Floating-Point Representation Format

## Slide 16: IEEE Standard for Binary Floating-Point Representation

## Slide 17: Machine Instruction Characteristics
Instructions it executes
The collection of different instructions that the processor can execute is referred to as the processor’s instruction set
4 Basic elements of an machine instruction
  Operation code
  Source operand reference
  Result operand reference
  Next instruction reference

## Slide 18: Elements of a Machine Instruction
Operation code: Specifies the operation to be performed (e.g., ADD, I/O)
  The operation is specified by a binary code, known as the operation code, or opcode
Source operand reference: The operation may involve one or more source operands, that is, operands that are inputs for the operation
Result operand reference: The operation may produce a result
Next instruction reference: This tells the processor where to fetch the next instruction after the execution of this instruction is complete

## Slide 19: Elements of a Machine Instruction
The address of the next instruction could be either-
  real address or
  a virtual address
Depends on architecture
Source and result operands can be in one of four areas:
Main or virtual memory: As with next instruction references, the main or virtual memory address must be supplied
Processor register: With rare exceptions, a processor contains one or more registers that may be referenced by machine instructions
  If only one register exists, reference to it may be implicit
  If more than one register exists, then each register is assigned a unique name or number, and the instruction must contain the number of the desired register

## Slide 20: Elements of a Machine Instruction
Immediate: The value of the operand is contained in a field in the instruction being executed
I/O device: The instruction must specify the I/O module and device for the operation
  If memory-mapped I/O is used, this is just another main or virtual memory address

## Slide 21: Instruction Representation
Each instruction is represented by a sequence of bits, within a computer
The instruction is divided into fields, corresponding to the constituent elements of the instruction
Opcodes are represented by abbreviations, called mnemonics, that indicate the operation
Some common examples-
ADD | Addition
SUB | Subtraction
DIV | Division
LOAD | Load data from memory
STOR | Store data to memory

## Slide 22: Instruction Representation
Operands are also represented symbolically
Example: ADD R, Y

## Slide 23: Instruction Types
A typical high level instruction
  X = X + Y
How is it done in low level/machine language?
A computer should have a set of instructions that allows the user to formulate any data processing task
The set of machine instructions must be sufficient to express any of the instructions from a high-level language
Basic types-
  Arithmetic instructions
  Logic (Boolean) instructions
  memory instructions
  I/O instructions
  Test instructions
  Branch instructions

## Slide 24: Number of Addresses
Arithmetic and logic instructions will require the most operands
Virtually all arithmetic and logic operations are either unary (one source operand) or binary (two source operands)
Thus, we would need a maximum of two addresses to reference source operands
The result of an operation must be stored, suggesting a third address, which defines a destination operand
Finally, after completion of an instruction, the next instruction must be fetched, and its address is needed
Zero-address instructions are applicable to a special memory organization, called a stack
Fewer addresses per instruction result in instructions that are more primitive, requiring a less complex processor

## Slide 25: Number of Addresses
The design trade-offs involved in choosing the number of addresses per instruction are complicated by other factors
There is the issue of whether an address references a memory location or a register
Because there are fewer registers, fewer bits are needed for a register reference
A machine may offer a variety of addressing modes, and the specification of mode takes one or more bits
With one-address instructions, the programmer generally has available only one general-purpose register, the accumulator
With multiple-address instructions, it is common to have multiple general purpose registers

## Slide 26: Instruction Set Design
Most fundamental issues include-
Operation repertoire: How many and which operations to provide, and how complex operations should be
Data types: The various types of data upon which operations are performed
Instruction format: Instruction length (in bits), number of addresses, size of various fields, and so on
Registers: Number of processor registers that can be referenced by instructions, and their use
Addressing: The mode or modes by which the address of an operand is specified

## Slide 27: Types of Operands
Important general categories are-
  Addresses
  Numbers
  Characters
  Logical data

## Slide 28: Types of Operations
General types-
  Data transfer
  Arithmetic
  Logical
  Conversion
  I/O
  System control
  Transfer of control
Data Transfer: The data transfer instruction must specify several things
  First, the location of the source and destination operands must be specified
  Each location could be memory, a register, or the top of the stack
  Second, the length of data to be transferred must be indicated
  Third, as with all instructions with operands, the mode of addressing for each operand must be specified

## Slide 29: Types of Operations
System Control
  System control instructions are those that can be executed only while the processor is in a certain privileged state or is executing a program in a special privileged area of memory
  Typically, these instructions are reserved for the use of the operating system
Transfer of Control
Why required?
In the practical use of computers, it is essential to be able to execute each instruction more than once and perhaps many thousands of times
  It may require thousands or perhaps millions of instructions to implement an application
  This would be unthinkable if each instruction had to be written out separately
  If a table or a list of items is to be processed, a program loop is needed
  One sequence of instructions is executed repeatedly to process all the data

## Slide 30: Types of Operations
Virtually all programs involve some decision making
  We would like the computer to do one thing if one condition holds, and another thing if another condition holds
  For example, a sequence of instructions computes the square root of a number
  At the start of the sequence, the sign of the number is tested
  If the number is negative, the computation is not performed, but an error condition is reported
To compose correctly a large or even medium-size computer program is an exceedingly difficult task
  It helps if there are mechanisms for breaking the task up into smaller pieces that can be worked on one at a time
Most common transfer-of-control operations found in instruction sets: branch, skip, and procedure call

## Slide 31: Branch Instructions
A branch instruction, also called a jump instruction, has as one of its operands the address of the next instruction to be executed
Most often, the instruction is a conditional branch instruction
That is, the branch is made (update program counter to equal address specified in operand) only if a certain condition is met
Otherwise, the next instruction in sequence is executed (increment program counter as usual)
A branch instruction in which the branch is always taken is an unconditional branch
Two ways of doing this:
  First, most machines provide a 1-bit or multiple-bit condition code that is set as the result of some operations
  This code can be thought of as a short user-visible register
  BRP X : Branch to location X if result is positive
  BRN X :Branch to location X if result is negative

## Slide 32: Branch Instructions
Another approach that can be used with a three-address instruction format is to perform a comparison and specify a branch in the same instruction
For example-
BRE R1, R2, X :Branch to X if contents of R1 = contents of R2
Fig: Branch Instructions

## Slide 33: Skip Instructions
The skip instruction includes an implied address
Typically, the skip implies that one instruction be skipped; thus, the implied address equals the address of the next instruction plus one instruction length
Because the skip instruction does not require a destination address field, it is free to do other things
A typical example is the increment-and-skip-if-zero (ISZ) instruction

## Slide 34: Procedure Call Instructions
A procedure is a self contained computer program that is incorporated into a larger program
At any point in the program the procedure may be invoked, or called
Used because of-
  Economy and
  Modularity
The procedure mechanism involves two basic instructions:
A call instruction that branches from the present location to the procedure, and a return instruction that returns from the procedure to the place from which it was called
  Both of these are forms of branching instructions

## Slide 35: Procedure Call Instructions
Important points:
  A procedure can be called from more than one location
  A procedure call can appear in a procedure
    This allows the nesting of procedures to an arbitrary depth
  Each procedure call is matched by a return in the called program

## Slide 36
Multiplication of Unsigned with example
Twos Complement Integers with example
Branch instruction with example
Skip instruction with example

## Slide 37: Thank you!